## Slide 1: Input and Output
By Crystal Hess

## Slide 2: Learning Goals
How to use a button
How to use a potentiometer
How to use an RGB LED
How to use a speaker

## Slide 3: Pair Programming

## Slide 4: Be a good pair partner

## Slide 5: Buttons (Digital Input)
Get the Button Example to work.
Change the code so that the LED turns OFF when you push the button and ON by default (opposite what it does now).
Add a second LED which is controlled by the same button.
Add a second button which controls the second LED. (Each button controls a separate LED).
Challenge
Open the Basics  Debounce Example and load it on your board. See what it does and play around with it.
Can you make your second button toggle the same way?

## Slide 6: Potentiometers (Analog Input)
Get the Fading Example to work. Add an external LED for pin 13.
Change the code to print out the sensorValue to the SerialMonitor. Observe what values are printed. Change the code so that the value printed stays between 0 and 256.
Change the code to use the sensorValue as the brightness for the LED instead of the delay time. (i.e. Make the potentiometer control the brightness of the LED.)
Challenge
Add a second LED which is controlled by the same potentiometer.
Add a second potentiometer to control the second LED.

## Slide 7: RGB LED (Output)
Complete this RGB tutorial.
What is the purpose of the setColor() method? Why is it useful?
Change the code:
  Remove all lines in the loop() method except the first line.
  Initialize a new variable int red = 255; under the pin initializations.
  Replace the first argument in the setColor call so that it reads setColor(red, 0, 0);
  Make sure the LED lights up as red.
Add a potentiometer to control the brightness of the red LED.
Challenge
Do the same for blue and green, so that you can control the color of the LED in real time.

## Slide 8: Speakers (Output)
Get the ToneMelody Example to work.
Using the image of notes on the next slide, change the code to play the first two lines of Jingle Bells.
Add a push button and trigger the tones when the button is pushed instead of at setup.
Challenge
Use an RGB LED to light up in sync with the music.